## Slide 1: CSCE 692 Design Principles of Computer Architecture Lecture 3 Appendix C – Pipelining
Dr. Scott Graham
AFIT/ENG
Notes adapted from
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley

## Slide 2: Datapath vs Control
Datapath: Storage, FU, interconnect sufficient to perform the desired functions
  Inputs are Control Points
  Outputs are signals
Controller: State machine to orchestrate operation on the data path
  Based on desired function and signals
Datapath
Controller
Control Points
signals
Notes: To begin, let us separate the concepts of a datapath, and the controller which manages the manipulation of data

## Slide 3: Approaching an ISA
Instruction Set Architecture
  Defines set of operations, instruction format, hardware supported data types, named storage, addressing modes, sequencing
Meaning of each instruction is described by RTL on architected registers and memory
Given technology constraints assemble adequate datapath
  Architected storage mapped to actual storage
  Function units to do all the required operations
  Possible additional storage (eg. MAR, MBR, …)
  Interconnect to move information among regs and FUs
Map each instruction to sequence of RTLs
Collate sequences into symbolic controller state transition diagram (STD)
Lower symbolic STD to control points
Implement controller
Notes: The controller also needs to be managed, or rather, told what it needs to accomplish. This requires a precise language, which is almost contractual. Through it, the software formally specifies what is required. Through it, the hardware offers precise services which it can actually achieve.
RTL: register transfer level
MAR: Memory address register
MBR: Memory buffer register

## Slide 4: 5 Steps of MIPS Datapath
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
L
M
D
ALU
MUX
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
4
Adder
Zero?
Next SEQ PC
Address
Next PC
WB Data
Inst
RD
RS1
RS2
Imm
IR <= mem[PC];
PC <= PC + 4
Reg[IRrd] <= Reg[IRrs] opIRop Reg[IRrt]
Notes: IF: Send PC to memory to fetch current instruction. Update PC=PC+4
ID: Decode Instr, read specified registers. Equality test on registers, sign-extend offset, compute possible branch target
EX: ALU either 1) Reg reg ALU, 2) reg imm ALU, 3)mem reference, so add base to offset -> effective address
MEM:
WB: write result (from ALU or mem) to reg

## Slide 5: 5 Steps of MIPS Datapath
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
Zero?
IF/ID
ID/EX
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX
IR <= mem[PC];
PC <= PC + 4
A <= Reg[IRrs];
B <= Reg[IRrt]
rslt <= A opIRop B
Reg[IRrd] <= WB
WB <= rslt
Notes: How do we pipeline the MIPS datapath? Just add water. Wait, pipeline registers.

## Slide 6: Inst. Set Processor Controller
IR <= mem[PC];
PC <= PC + 4
A <= Reg[IRrs];
B <= Reg[IRrt]
r <= A opIRop B
Reg[IRrd] <= WB
WB <= r
Ifetch
opFetch-DCD
PC <= IRjaddr
if bop(A,b)
PC <= PC+IRim
br
jmp
RR
r <= A opIRop IRim
Reg[IRrd] <= WB
WB <= r
RI
r <= A + IRim
WB <= Mem[r]
Reg[IRrd] <= WB
LD
ST
JSR
JR
Issue

## Slide 7: Visualizing Pipelining
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5

## Slide 8: Pipelining is not quite that easy!
Limits to pipelining: Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: HW cannot support this combination of instructions
  Data hazards: Instruction depends on result of prior instruction still in the pipeline
  Control hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow (branches and jumps).

## Slide 9: One Memory Port/Structural Hazards
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg

## Slide 10: One Memory Port/Structural Hazards
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
How do you “bubble” the pipe?

## Slide 11: Speed Up Equation for Pipelining
For simple RISC pipeline, Ideal CPI = 1:

## Slide 12: Data Hazard on R1
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 13: Three Generic Data Hazards
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Caused by “True Dependency” (in compiler nomenclature). This hazard results from an actual need for communication.
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 14: Three Generic Data Hazards
Write After Read (WAR) InstrJ writes operand before InstrI reads it
Called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Reads are always in stage 2, and
  Writes are always in stage 5
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 15: Three Generic Data Hazards
Write After Write (WAW) InstrJ writes operand before InstrI writes it.
Called an “output dependence” by compiler writers This also results from the reuse of name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Writes are always in stage 5
Will see WAR and WAW in more complicated pipes
I: sub r1,r4,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 16: Forwarding to Avoid Data Hazard
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 17: HW Change for Forwarding
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux
What circuit detects and resolves this hazard?
Notes: Note the Forwarding Unit resides in the EX stage and “quickly” tests for the RAW and then controls the mux inputs into the ALU.
Detects by:
ID/EX.rs or rt = EX/MEM.rd (1 instr behind)
ID/EX.rs or rt = MEM/WR.rd (2 instr behind)

## Slide 18
So, we insert a forwarding unit into the processor
  Works real well if insts only 1 or 2 apart. What about 3?
P
C
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
R
e
g
i
s
t
e
r
s
M
u
x
M
u
x
C
o
n
t
r
o
l
A
L
U
E
X
M
W
B
M
W
B
W
B
I
D
/
E
X
E
X
/
M
E
M
M
E
M
/
W
B
D
a
t
a
m
e
m
o
r
y
M
u
x
F
o
r
w
a
r
d
i
n
g
u
n
i
t
I
F
/
I
D
I
n
s
t
r
u
c
t
i
o
n
M
u
x
R
d
E
X
/
M
E
M
.
R
e
g
i
s
t
e
r
R
d
M
E
M
/
W
B
.
R
e
g
i
s
t
e
r
R
d
R
t
R
t
R
s
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
d
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
s
    EX/MEM.WriteReg == ID/EX.ReadReg1 or 2 (Forward)
    MEM/WB.WriteReg == ID/EX.ReadReg1 or 2 (Forward)

## Slide 19: Pipeline_Matrix.xlsx
Instructions | Operands | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ld | x1, 0(x2) | IF | ID | EX | M | WB |  |  |  |  | 
addi | x1, x1, x3 |  | IF |  |  |  |  |  |  |  | 

## Slide 20: Pipeline_Matrix.xlsx
Instructions | Operands | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
ld | x1, 0(x2) | IF | ID | EX | M | WB |  |  |  |  | 
addi | x1, x1, x3 |  | IF | ID | - | id | EX | M | WB |  | 
 |  |  |  | IF | - | - | ID |  |  |  | 

## Slide 21: Forwarding to Avoid LW-SW Data Hazard
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
lw r4, 0(r1)
sw r4,12(r1)
or r8,r6,r9
xor r10,r9,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 22: Data Hazard Even with Forwarding
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Notes: MIPS actually didn’t interlock: MPU without Interlocked Pipelined Stages

## Slide 23: Data Hazard Even with Forwarding (Similar to Figure A.10, Page A-21)
Time (clock cycles)
or r8,r1,r9
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
Ifetch
ALU
DMem
Bubble
Reg
How is this detected?
Notes: Hazard Detection unit in ID stage
  Test for If (ID/EX.MemRead) AND
    (ID/EX.WriteReg == IF/ID.ReadReg1 or 2) then Stalll
    If need to stall put 0’s in ID/EX reg (nop) and re-decode instruction and re-fetch next instruction.

## Slide 24
Let’s add the hazard detection unit to the design
P
C
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
R
e
g
i
s
t
e
r
s
M
u
x
M
u
x
M
u
x
C
o
n
t
r
o
l
A
L
U
E
X
M
W
B
M
W
B
W
B
I
D
/
E
X
E
X
/
M
E
M
M
E
M
/
W
B
D
a
t
a
m
e
m
o
r
y
M
u
x
H
a
z
a
r
d
d
e
t
e
c
t
i
o
n
u
n
i
t
F
o
r
w
a
r
d
i
n
g
u
n
i
t
0
M
u
x
I
F
/
I
D
I
n
s
t
r
u
c
t
i
o
n
I
D
/
E
X
.
M
e
m
R
e
a
d
I
F
/
I
D
W
r
i
t
e
P
C
W
r
i
t
e
I
D
/
E
X
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
d
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
t
I
F
/
I
D
.
R
e
g
i
s
t
e
r
R
s
R
t
R
s
R
d
R
t
E
X
/
M
E
M
.
R
e
g
i
s
t
e
r
R
d
M
E
M
/
W
B
.
R
e
g
i
s
t
e
r
R
d
Note the mux to insert 0s into control fields of ID/EX reg
  If (ID/EX.MemRead) AND
    (ID/EX.WriteReg == IF/ID.ReadReg1 or 2) then Stall

## Slide 25: Software Scheduling to Avoid Load Hazards
Fast code:
LW Rb,b
LW Rc,c
LW Re,e
ADD Ra,Rb,Rc
LW Rf,f
SW a,Ra
SUB Rd,Re,Rf
SW d,Rd
Try producing fast code for
a = b + c;
d = e – f;
assuming a, b, c, d ,e, and f in memory.
Slow code:
LW Rb,b
LW Rc,c
ADD Ra,Rb,Rc
SW a,Ra
LW Re,e
LW Rf,f
SUB Rd,Re,Rf
SW d,Rd
Compiler optimizes for performance. Hardware checks for safety.

## Slide 26: Control Hazard on Branches Three Stage Stall
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
What do you do with the 3 instructions in between?
How do you do it?
Where is the “commit”?

## Slide 27: Branch Stall Impact
If CPI = 1, 30% branch, Stall 3 cycles => new CPI = 1.9!
Two part solution:
  Determine branch taken or not sooner, AND
  Compute taken branch address earlier
MIPS branch tests if register = 0 or  0
MIPS Solution:
  Move Zero test to ID/RF stage
  Adder to calculate new PC in ID/RF stage
  1 clock cycle penalty for branch versus 3
Notes: Note can compare with the XOR  OR

## Slide 28: Pipelined MIPS Datapath
Adder
IF/ID
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
Data
Memory
MUX
Sign
Extend
Zero?
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
RD
RD
RD
WB Data
Interplay of instruction set design and cycle time.
Next PC
Address
RS1
RS2
Imm
MUX
ID/EX

## Slide 29: Four Branch Hazard Alternatives (static)
#1: Stall until branch direction is clear
#2: Predict Branch Not Taken
  Execute successor instructions in sequence
  “Squash” instructions in pipeline if branch actually taken
  Advantage of late pipeline state update
  47% MIPS branches not taken on average
  PC+4 already calculated, so use it to get next instruction
#3: Predict Branch Taken
  53% MIPS branches taken on average
  But haven’t calculated branch target address in MIPS
    MIPS still incurs 1 cycle branch penalty
    Other machines: branch target known before outcome
Notes: Static: decided at compile time
Dynamic: run-time choices or actions/reactions based on static choices.

## Slide 30: Four Branch Hazard Alternatives
#4: Delayed Branch
  Define branch to take place AFTER a following instruction
  branch instruction sequential successor1 sequential successor2 ........ sequential successorn
  branch target if taken
  1 slot delay allows proper decision and branch target address in 5 stage pipeline
  MIPS uses this
Branch delay of length n

## Slide 31: Scheduling Branch Delay Slots
A is the best choice, fills delay slot & reduces instruction count (IC)
In B, the sub instruction may need to be copied, increasing IC
In B and C, must be okay to execute sub when branch fails
  (e.g. a temp value only used in that respective code section)
add $1,$2,$3
if $2=0 then
delay slot
A. From before branch
B. From branch target
C. From fall through
add $1,$2,$3
if $1=0 then
delay slot
add $1,$2,$3
if $1=0 then
delay slot
sub $4,$5,$6
sub $4,$5,$6
becomes
becomes
becomes
if $2=0 then
add $1,$2,$3
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
sub $4,$5,$6
Notes: Limitations on delayed-branch scheduling come from 1) restrictions on the instructions that can be moved/copied into the delay slot and 2) limited ability to predict at compile time whether a branch is likely to be taken or not.
In B and C, the use of $1 prevents the add instruction from being moved to the delay slot
In B the sub may need to be copied because it could be reached by another path. B is preferred when the branch is taken with high probability (such as loop branches

## Slide 32: Delayed Branch (static)
Compiler effectiveness for single branch delay slot:
  Fills about 60% of branch delay slots
  About 80% of instructions executed in branch delay slots useful in computation
  About 50% (60% x 80%) of slots usefully filled
Delayed Branch downside: As processor go to deeper pipelines and multiple issue, the branch delay grows and need more than one delay slot
  Delayed branching has lost popularity compared to more expensive but more flexible dynamic approaches
  Growth in available transistors has made dynamic approaches relatively cheaper

## Slide 33: Problems with Pipelining
Exception: An unusual event happens to an instruction during its execution
  Examples: divide by zero, undefined opcode
Interrupt: Hardware signal to switch the processor to a new instruction stream
  Example: a sound card interrupts when it needs more audio output samples (an audio “click” happens if it is left waiting)
Problem: It must appear that the exception or interrupt appear between 2 instructions (Ii and Ii+1)
  The effect of all instructions up to Ii must complete
  No effect of Ii and any instruction after Ii can take place
The interrupt (exception) handler either aborts program or restarts at instruction Ii+1

## Slide 34: Exceptions
According to the authors, handling hazards was easy
  Now we get to do the hard stuff - exceptions
Definition: Exception is used to mean any exceptional situation which occurs, regardless of whether it was done deliberately or whether it indicates an error condition
  Encompasses terms trap, interrupt, and fault
  Includes things like software interrupts, page faults, and arithmetic overflow

## Slide 35: Exceptions
Exceptions can be caused by a wide variety of circumstances
Text categorizes exceptions according to 5 characteristics
  1. Synchronous (occurs at same place/time) vs. asynchronous (external event)
  2. User requested or coerced (hardware)
  3. User maskable or nonmaskable
  4. Occurs within or between instructions
  5. Resume execution or terminate process (How does program respond after exception?)
Last two characteristics most critical to how exception is handled
  Figure C.26 - summarizes exception examples vs. categories
Notes: 1. Synchronous (occurs at same place/time): same data and sequence always raises exception
2. User requested: user program creates the exception (internal to code sequence)
3. User maskable or nonmaskable: can I choose to ignore (e.g., addu)
4. Occurs within or between instructions
Resume execution or terminate process (How does program respond after exception?)
  Termination easier to implement although now more processors leaning toward resuming (req for VM)

## Slide 36: Exceptions
Exceptions like “O/S time slice expired” aren’t terribly difficult to handle
  It doesn’t occur within instruction
    Can just vector execution to an O/S routine, and allow all ongoing instructions to complete
But exceptions which occur within an instruction and for which execution must be resumed are very difficult to handle correctly
  The reason is the need for precise exceptions
    Pipeline can be halted and restarted after handler
      All instructions prior to excepting instruction should complete
      Excepting instruction and others following don’t alter program state
    Multiple exceptions handled in sequential order
Notes: Precise exceptions often >10 times slower so may want to force imprecise.

## Slide 37: Exceptions
What to do when exception occurs within an instruction?
  Halt execution of excepting instruction and subsequent instructions
    Turn off writes for excepting and following instructions
  Allow instructions ahead of the excepting instruction to complete
  Save PC and reason for exception
  Trap to exception handler
    In MIPS, done by inserting trap instruction into IF
  Above steps sometimes called “draining the pipeline”

## Slide 38: Exceptions
Why is handling exceptions hard?
  The excepting instruction, or one behind it, may have already changed machine state before the exception is detected
    Auto-incrementing memory ops
  Exceptions must be handled in original sequential program order
    An instruction in IF may have a page fault, which occurs in time prior to an page fault in the MEM stage from the preceding instruction
  Some instructions which cause a fault maybe shouldn’t have been executed
    If have IF page fault on predict-not-taken instruction, don’t want to handle if branch is taken

## Slide 39: Exceptions
Before we define a solution for the MIPS architecture, let’s look at the types of exceptions MIPS must handle

## Slide 40: Exceptions
How do we handle MIPS exceptions?
  In MIPS, instructions only change machine state in MEM or WB stage
    Since all exceptions occur during MEM or earlier, we should be able to detect all exceptions prior to the instruction changing state
  To ensure exceptions occur in sequential order, we delay exception handling for all instructions until the beginning of the WB stage
    If an instruction has an exception earlier in the pipeline, we record it in an exception status field which flows through pipe with the instruction
    When instruction reaches WB, exceptions handled in proper order

## Slide 41: Exceptions
Other complications to precise exceptions
  Instructions which change state earlier
    Auto-increment
    Implicit condition codes
  CISC instructions which change lots of registers or memory values
    X86 string copy
  Instructions completing out-of-order (next section)

## Slide 42: Precise Exceptions in Static Pipelines
Key observation: architected state only change in memory and register write stages.

## Slide 43: Multicycle Operations
It’s time to leave the simple CSCE 092/492 pipeline behind, and get on with the more realistic stuff
First item is how to handle multi-cycle operations
  Need to be able to do multiply and FP ops
  Can’t slow the clock rate so that the FP multiply only takes one cycle in EX (recall critical path)
  So, some instructions are going to have to spend many cycles in EX
  Two choices
    Halt the pipeline (no one leaves ID phase) until long-running instruction finished EX
    Let other instructions execute in parallel with the long-running instruction

## Slide 44: Multicycle Operations
Halting the pipeline example
  CPI_int = 1 cc FP add = 4 cycles FP mult = 8 cycles
  Int_ops = 80% FP add = 10% FP mult = 10%
  CPI = 1 + .1 (3) + .1 (7) = 2 (Blue numbers = additional cycles required)
    FP ops halved performance
    Can you rewrite the above equation in more natural terms?
Notes: Better way to write equation based on how long each took: .8(1cc) + .1(4cc) + .1 (8cc) = 2.0 cc

## Slide 45: Multicycle Operations
Note that the pipeline has multiple functional units (FU), but only one is being used at a time
  We would like to exploit parallelism available in H/W
  So, if a FP multiply is going on, and the instruction in ID needs the integer ALU, let’s let it proceed on
IF ID
Mem WB
EX
EX
EX
EX
int
FP add
FP mul
FP div

## Slide 46: Multicycle Operations
By allowing instructions to proceed if the FU they need is available, we can keep the pipeline busier, and hopefully we can keep one instruction moving from ID to EX each cycle
  Now we measure throughput of machine by how many instructions we can move from ID to EX each cycle on average
    Hopefully this is near one for current design
    Throughput can also be measured by how many instructions finish WB each cycle
  This concept is why we talk about instruction issue
    An instruction issues when it moves from ID to EX

## Slide 47: Multicycle Operations
Issuing instructions to a free FU when another long-running instruction is executing greatly increases performance
  But we still have a problem if two FP multiplies come in right after another
    The second mult is going to be stuck in ID, and going to block the pipeline due to the structural hazard
    What did we say earlier was the solution?
      Pipeline the FU, so it can start a new operation each cycle
M1
M2
M3
M4
M5
M6
M7
FP multiply

## Slide 48: Multicycle Operations
Recall that pipelining may incur a time overhead
  If have 10ns clock cycle, and multiply takes 79ns
    Pipelining unit may require an increase from 8 cycles to 9 due to the overhead time
  So, need to do a tradeoff study to decide whether to pipeline multiply
  As a result, may decide to pipeline some FUs and not others
Notes: If the clock is 10ns & multiply execution takes 79ns then would require 8 pipelined cyles (80ns), but due to the overhead of the pipeline may actually need more than 80ns and have to add a 9 cc to the new multiply sub-pip.

## Slide 49: Multicycle Operations
New MIPS pipeline and instruction timing
IF
ID
MEM
WB
1
Integer Unit
FP/integer multiply
FP adder
FP/integer divider
M1
M2
M3
M4
M5
M6
M7
EX
A1
A2
A3
A4
DIV
24
Divide is not pipelined but requires 24 cycles to execute

## Slide 50: Multicycle Operations
MIPS timing (assume forwarding)
  Latency - Number of intervening cycles between the instruction which produces a result and an instruction which uses the result
    Usually the number of stages after EX that instruction produces result
    Essentially sub-pipeline depth - 1
    Not necessarily a standard definition of latency
  Initiation interval - how frequently instructions can be sent to the FU. Is there a problem in the FP div initiation interval?
Functional Unit Latency Initiation Interval
Integer ALU 0 1
Data memory (integer and FP loads) 1 1
FP Add 3 1
FP multiply (and integer multiply) 6 1
FP divide (and integer divide) 24 23 25 24
Notes: FP divide is not sub-piped while the rest are.
Assume forwarding here. (functional unit output to functional unit input) (exex, M7M1, A1A4)
Edition 6 continues the “error” showing latency of 24 and interval of 25. Having read through both editions, I (Dr. Graham) see no support for a latency of 24 and interval of 25.

## Slide 51: Multicycle Operations
New MIPS pipeline and instruction timing
MUL.D IF ID M1 M2 M3 M4 M5 M6 M7 MEM WB
ADD.D IF ID A1 A2 A3 A4 MEM WB
L.D IF ID EX MEM WB
S.D IF ID EX MEM WB
Operands Needed
Result Available
Notes: Out of order completion
Can have WAW now
Still safe from WAR

## Slide 52: Multicycle Operations
We have created some significant problems with our new design
  Hazards and forwarding is gonna be tougher
    New structural hazards, plus new data hazards
  Precise exceptions is big problem
    We are now letting instructions complete out-of-order
      Still in-order issue and in-order execution
    How do you restart after an exception?

## Slide 53: Multicycle Operations
New structural hazards
  Non-availability of a FU
    Obviously, it can occur for the FP div unit, which is not pipelined
    Can it happen for other FU units?
    Should be relatively straightforward to detect hazard and stall pipe
  Contention for entering WB stage (potentially MEM)
    Since different instructions execute different number of cycles, frequently 2 will finish at same time
    Note that MEM may overlap but not all operations use MEM (e.g., add vs. ld)
    What do you do?

## Slide 54: Multicycle Operations
Example of multiple instructions arriving at MEM/WB
Two solutions
  Multiple write ports into register file
    Int and FP already separate register files
  Detect problem and interlock on structural hazard
MUL.D IF ID M1 M2 M3 M4 M5 M6 M7 MEM WB
Cycle 1 2 3 4 5 6 7 8 9 10 11
… IF ID EX MEM WB
ADD.D IF ID A1 A2 A3 A4 MEM WB
… IF ID EX MEM WB
… IF ID EX MEM WB
L.D IF ID EX MEM WB
… IF ID EX MEM WB

## Slide 55: Multicycle Operations
Contention for MEM/WB - structural hazard interlock
  Two approaches to interlocking
    Detect hazard when instruction tries to enter MEM/WB
      Stall shortest-latency instruction
      Easy to detect at this point, but harder to fix
    Don’t allow instruction to issue if it would cause this hazard
      Requires use of a shift register which keeps track of availability of MEM/WB stages
      When instruction issues, it reserves a slot in shift reg
      If no slot available when the instruction would arrive at MEM/WB, then stall the instruction at issue
      Harder to detect, but all stalls now done at issue

## Slide 56: Multicycle Operations
We don’t allow instruction to issue if a structural hazard exists
  Also don’t want to allow it to issue if a data hazard exists
    RAW hazards
      We still have the problem of a 1 cycle stall on loads
      Recall the latencies of FP ops
        FP add - 3 cycles
        FP mult - 6 cycles
        FP div - 24 cycles
      So, an instruction less than 7 cycles behind a FP multiply will have a data hazard
        Need much more extensive RAW hazard detection

## Slide 57: Multicycle Operations
Timing of MIPS FP ops
  For FP multiply, result done in M7, but may be needed in A1
  Cannot issue any instruction which uses the result being defined in M1 - M6; can forward from M7
  Earlier in chapter, only had to compare ID/EX source operands to destinations in EX/MEM and MEM/WB
    Now must compare to M1-M6, A1-A3, FPDIV for stall
    Compare to M7, A4, and FPDIV (if done) for forward
MUL.D IF ID M1 M2 M3 M4 M5 M6 M7 MEM WB
ADD.D IF ID A1 A2 A3 A4 MEM WB
L.D IF ID EX MEM WB
S.D IF ID EX MEM WB
Operands Needed
Result Available

## Slide 58: Multicycle Operations
Stalls resulting from RAW hazards
  Each instruction requires previous result
  Depending on actual machine structure SD (MEM) may occur in clock cycle 16 if additional write port available or 17 if not available
Clock Cycle
Instruction
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
L.D F4, 0(R2)
IF
ID
EX
MEM
WB
MUL.D F0,
F4
, F6
IF
stall
M1
M2
M3
M4
M5
M6
M7
MEM
WB
ADD.D F2,
F0
, F8
IF
stall
ID
stall
stall
stall
stall
stall
stall
A1
A2
A3
A4
S.D
F2
, 0(R2)
IF
stall
stall
stall
stall
stall
stall
ID
EX
stall
stall
ID
16
MEM
stall

## Slide 59: Multicycle Operations
Now have to consider WAW and WAR hazards
  WAW hazard
    Consider code sequence below
      If we don’t check for WAW hazard, we get wrong answer
        How do we fix this?
      What would have happened if there was an intervening use of F2?
MUL.D F0, F4, F6
ADD.D F2, F4, F6 ADD.D F1, F2, F3
L.D F2, 0(R2)
Clock Cycle
Instruction
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
MUL.D F0, F4, F6
IF
ID
ADD.D F2, F4, F6
IF
L.D F2, 0(R2)
IF
ID
A1
A2
A3
A4
EX
stall
stall
ID
16
MEM
stall
MEM
M1
M2
M3
M4
M5
M6
M7
MEM
WB
WB
WB

## Slide 60: Multicycle Operations
WAW will not exist if intervening read on same register
Clock Cycle
Instruction
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
MUL.D F0, F4, F6
IF
ID
ADD.D F2, F4, F6
IF
L.D F2, 0(R2)
IF
ID
A1
A2
A3
A4
stall
stall
ID
16
MEM
stall
M1
M2
M3
M4
M5
M6
M7
MEM
WB
WB
ADD.D F1, F2, F3
A1
A2
A3
A4
MEM
WB
IF
ID
stall
stall
EX
MEM
WB
Will WAR occur above now on F2?
  When are operands read?
  Is there any way the L.D could execute before ADD.D reads operands?
WAR hazards not a problem for current MIPS architecture
  In Chap 3 will see architectures where WARs occur

## Slide 61: Multicycle Operations
OK, so now we’ve handled structural and data hazards
  Now we address the bigger problem: how to maintain precise interrupts
  Precise Interrupts
    1: All instructions prior to excepting instruction should complete
    2: Excepting instruction and following don’t alter program state
    3: Multiple exceptions handled in sequential order
Consider code sequence below; how would it execute?
  Even with accurate hazard detection, the ADD.D and SUB.D will both complete before the DIV.D
    This is known as out-of-order completion
    What happens if the SUB.D has an exception and later DIV.D does?
      Shouldn’t handle SUB.D yet since DIV.S not done (Violates 3)
      ADD.D already updated registers (Violates 2)
      How do we restart after the exception is handled?
DIV.D F0, F2, F4
ADD.D F10, F10, F8
SUB.D F12, F12, F14

## Slide 62: Precise Exceptions
This is a big problem, which only gets worse in Chap 3 as we really start reordering
Four common approaches:
  #1 Don’t support precise interrupts
    Not a good solution - IEEE 754 requires it
    Some current architectures have dual mode
      In precise mode, essentially forces in-order completion
  #2 Save enough state to restart pipeline where it was
    Basically requires state of every ongoing instruction to be stored
    Machines usually limit how many can be concurrently executing

## Slide 63: Precise Exceptions
Approaches to maintaining precise exceptions (cont)
  #3 Only issue instructions if all prior instructions are sure not to cause exception
    If exception occurs, guaranteed that:
      No instructions after excepting inst have completed
      All instructions before excepting inst can complete
    Functional units check for possible exception as early as possible
    Used in R3000, R4000, and Pentium

## Slide 64: Precise Exceptions
Approaches to maintaining precise exceptions (cont)
  #4 Buffer results of operations until all operations that were issued earlier are complete
    Instruction is done, but machine not fully committed to it until all earlier issued instructions are done
    Two major approaches
        History file (save original value of destination register for roll back)
        Future file (save future value of register, when earlier instructions finish, update registers)
    Due to amount of buffering, may not seem worthwhile for present pipeline
        Future file becomes critical for dynamically scheduled machines

## Slide 65: Precise Exceptions
History file (buffer)
  When an instruction issues, the value in its destination register is stored in the history buffer
  When instruction issues, it is also placed in a retirement queue
    When instruction completes, entry in queue marked valid
Register
File
History
Buffer
Result Bus
Source Data
Retire
Queue

## Slide 66: Precise Exceptions
  Reading of data is from the register file
    Always gets latest value
  Each cycle, examine the head of queue
    If no exception and valid, delete queue entry and history buffer entry
    If exception, any entry behind it in queue marked valid will require its value corrected from history buffer
Retire Queue
Tag Dest Valid Exception
1 0
1 1
1 0
0 0
1 0
3
5
4
0
2
0
1
2
3
4
Register
File
History
Buffer
Result Bus
Source Data

## Slide 67: Precise Exceptions
Future file
  Similar to history buffer
  Future file doesn’t update register file until instruction retired
    On exception, register file correct
  Completing instructions update future file
    On retire, contents of future file update permanent register file
    Values fetched from future file
Future
File
Register
File
Result Bus
Source Data
Retire
Queue
To register save