## Slide 1
CSCE 692 Design Principles of Computer Architecture Lecture 4b Chap 3 – Tomasulo Algorithm
Dr. Scott Graham
AFIT/ENG
Notes adapted from
David Patterson
Electrical Engineering and Computer Sciences
University of California, Berkeley

## Slide 2: Advantages of Dynamic Scheduling
Dynamic scheduling - hardware rearranges the instruction execution to reduce stalls while maintaining data flow and exception behavior
It handles cases when dependences unknown at compile time
  it allows the processor to tolerate unpredictable delays such as cache misses, by executing other code while waiting for the miss to resolve
It allows code that compiled for one pipeline to run efficiently on a different pipeline
It simplifies the compiler
Hardware speculation, a technique with significant performance advantages, builds on dynamic scheduling (next lecture)

## Slide 3: HW Schemes: Instruction Parallelism
Key idea: Allow instructions behind stall to proceed DIVD F0,F2,F4 ADDD F10,F0,F8 SUBD F12,F8,F14
Enables out-of-order execution and allows out-of-order completion (e.g., SUBD)
  In a dynamically scheduled pipeline, all instructions still pass through issue stage in order (in-order issue)
Out-of-order completion caused WAW
Out-of-order execution causes WAR

## Slide 4: Why Tomasulo Algorithm?
Implemented for the floating point unit of the IBM 360/91
  About 3 years after CDC 6600 (1966)
Goal: High Performance without special compilers
Differences between IBM 360 & CDC 6600 ISA
  IBM has only 2 register specifiers/instruction vs. 3 in CDC 6600
  IBM has 4 FP registers vs. 8 in CDC 6600
  Pipelined rather than multiple functional units (but conceptually viewed as multiple functional units)
    Adder supports 3 instructions
    Multiplier supports 2 instructions
Why Study? lead to Alpha 21264, HP 8000, MIPS 10000, Pentium II, PowerPC 604, i7

## Slide 5: Tomasulo Algorithm
Hardware will detect and preserve dependencies (within a limited window of the instruction stream)
Hardware will check for resource availability
Independent instructions will be issued to the correct functional units
Correctness of execution guaranteed by hardware
Independent of compiler optimizations
Backward compatibility
  Software scheduling: different machine configuration necessitate recompilation (or at least rescheduling)

## Slide 6: Tomasulo Algorithm
Control & buffers distributed with Function Units (FU)
  FU buffers called “reservation stations”; have pending operands
Registers in instructions replaced by values or pointers to reservation stations(RS); called register renaming ;
  Renaming avoids WAR, WAW hazards
  More reservation stations than registers, so can do optimizations compilers can’t
Results to FU from RS, not through registers, over Common Data Bus that broadcasts results to all FUs
  Avoids RAW hazards by executing an instruction only when its operands are available
Load and Stores treated as FUs with RSs as well
Integer instructions can go past branches (predict taken), allowing FP ops beyond basic block in FP queue

## Slide 7: Tomasulo Organization
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 8: Reservation Station Components
Op—Operation to perform in the unit (e.g., + or –) on S1 and S2
Vj, Vk—Value of source operands
  Either V or Q is valid for each operand
Qj, Qk—Reservation stations producing source registers (value to be written)
  Note: No ready flags as in Scoreboard; Qj, Qk=0 => ready
  Store buffers only have Qi for RS producing result
Busy—Indicates reservation station or FU is busy
Register result status—Indicates which functional unit (Qi) will write each register, if one exists. Blank when no pending instructions that will write that register.

## Slide 9: Reservation Station Components
The format is essentially:
OPR.D Qi, Qj, Qk
Qi, Qj, and Qk Are essentially tags
Qi is not a register tag, it’s tags the FU producing the result
VALUES for Qj and Qk are held in Vj and Vk
Register result is literally a list where each element in the list refers to a FP Register and each value of each element is either blank or e.g., ADD1, ADD2, ADD3, MUL1, MUL2, DIV

## Slide 10: Three Stages of Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues instruction & sends operands (renames registers).
2. Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available
Normal data bus: data + destination (“go to” bus)
Common data bus: data + source (“come from” bus)
  Does the broadcast
  64 bits of data + 4 bits of Functional Unit source address
  FU snags value on CDB if matches expected FU (produces result)
Notes: For Issue: Note that remaining registers avoids name dependencies (anti-WAR and output-WAW)
For Execution, RAW eliminated since result is directly pulled off the bus and stored in the associated reservation station.

## Slide 11: Detailed Tomasulo Pipeline Control
Execute
Instruction status
Write result
Issue
Bookkeeping
None — operands are in Vj and Vk
x(if (RegisterStat[x].Qi=r)
{Regs[x]  result; RegisterStat[x].Qi  0}); x(if (RS[x].Qj=r) {RS[x].Vj  result; RS[x].Qj  0}); x(if (RS[x].Qk=r) {RS[x].Vk  result; RS[x].Qk  0}); RS[r].Busy  No
if (RegisterStat[‘S1’].Qi  0)
{RS[r].Qj  RegisterStat[‘S1’].Qi}
else {RS[r].Vj  S1; RS[r].Qj  0}
if (RegisterStat[‘S2’].Qi  0)
{RS[r].Qk  RegisterStat[‘S2’].Qi}
else {RS[r].Vk  S2; RS[r].Qk  0}
RS[r].Busy  yes;
RegisterStat[‘D’].Qi  r;
(RS[r].Qj=0) and
(RS[r].Qk=0)
Wait until
Execution completed
at r
and CDB available
Station or
buffer empty
r = RS instruction is assigned

## Slide 12: Tomasulo Example Cycle 0
Qi
ASSUME ‘EX’ CC’s: Load-2, Add-2, Mult-10, Div-40
3 Load/Buffers
3 FP Adder R.S.
2 FP Mult R.S.

## Slide 13: Tomasulo Example Cycle 1

## Slide 14: Tomasulo Example Cycle 2
Note: Unlike 6600, can have multiple loads outstanding

## Slide 15: Tomasulo Example Cycle 3
Note: register names are removed (“renamed”) in Reservation Stations; MULT issued vs. scoreboard
Load1 completing

## Slide 16: Tomasulo Example Cycle 4
Load2 completing; what is waiting for it?

## Slide 17: Tomasulo Example Cycle 5
Instruction status
Execution
Write
Instruction
j
k
Issue
complete
Result
RS (Q)
Busy
Address
L.D
F6
34+
R2
1
3
4
Load1
No
L.D
F2
45+
R3
2
4
5
Load2
No
MUL.D
F0
F2
F4
3
Load3
No
SUB.D
F8
F6
F2
4
DIV.D
F10
F0
F6
5
ADD.D
F6
F8
F2
Reservation Stations (Q)
S1
S2
RS for Vj
RS for Vk
Time
Name
Busy
Op
Vj
Vk
Qj
Qk
2
Add1
Yes
SUB.D
R(F6)
M(45+R3)
0
0
0
Add2
No
0
Add3
No
10
Mult1
Yes
MUL.D
M(45+R3)
R(F4)
0
0
0
Mult2
Yes
DIV.D
R(F6)
Mult1
0
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
5
FU
Mult1
M(45+R3)->0
Add1
Mult2

## Slide 18: Tomasulo Example Cycle 6
Issue ADD.D here vs. scoreboard?

## Slide 19: Tomasulo Example Cycle 7
Add1 completing; what is waiting for it?

## Slide 20: Tomasulo Example Cycle 8

## Slide 21: Tomasulo Example Cycle 9

## Slide 22: Tomasulo Example Cycle 10
Add2 completing; what is waiting for it?

## Slide 23: Tomasulo Example Cycle 11
Write result of ADD.D here vs. scoreboard?
Notes: No WAR on DIV.D since DIV has value directly stored in Vk (as opposed to having to wait and read the register).

## Slide 24: Tomasulo Example Cycle 12
Note: all quick instructions complete already

## Slide 25: Tomasulo Example Cycle 13
Instruction status
Execution
Write
Instruction
j
k
Issue
complete
Result
RS (Q)
Busy
Address
L.D
F6
34+
R2
1
3
4
Load1
No
L.D
F2
45+
R3
2
4
5
Load2
No
MUL.D
F0
F2
F4
3
Load3
No
SUB.D
F8
F6
F2
4
7
8
DIV.D
F10
F0
F6
5
ADD.D
F6
F8
F2
6
10
11
Reservation Stations (Q)
S1
S2
RS for Vj
RS for Vk
Time
Name
Busy
Op
Vj
Vk
Qj
Qk
0
Add1
No
0
Add2
No
0
Add3
No
2
Mult1
Yes
MUL.D
M(45+R3)
R(F4)
0
0
0
Mult2
Yes
DIV.D
R(F6)
Mult1
0
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
13
FU
Mult1
Mult2

## Slide 26: Tomasulo Example Cycle 14

## Slide 27: Tomasulo Example Cycle 15
Mult1 completing; what is waiting for it?

## Slide 28: Tomasulo Example Cycle 16
Note: Just waiting for divide

## Slide 29: Tomasulo Example Cycle 55 – TIME Warp!!

## Slide 30: Tomasulo Example Cycle 56
Mult 2 completing; what is waiting for it?

## Slide 31: Tomasulo Example Cycle 57
Again, in-order issue, out-of-order execution, completion

## Slide 32: Compare to Scoreboard Cycle 62
Why does it take longer on Scoreboard/6600?
Instruction status
Read
Execution
Write
Instruction
j
k
Issue
operands
complete
Result
L.D
F6
34+
R2
1
2
3
4
L.D
F2
45+
R3
5
6
7
8
MUL.D
F0
F2
F4
6
9
19
20
SUB.D
F8
F6
F2
7
9
11
12
DIV.D
F10
F0
F6
8
21
61
62
ADD.D
F6
F8
F2
13
14
16
22
Functional unit status
dest
S1
S2
FU for j
FU for k
Fj?
Fk?
Time
Name
Busy
Op
Fi
Fj
Fk
Qj
Qk
Rj
Rk
Integer
No
Mult1
No
Mult2
No
Add
No
0
Divide
No
Register result status
Clock
F0
F2
F4
F6
F8
F10
F12
...
F30
62
FU

## Slide 33: Tomasulo vs. Scoreboard (IBM 360/91 vs. CDC 6600)
Pipelined Functional Units Multiple Functional Units
(6 load, 3 store, 3 +, 2 x/÷) (1 load/store, 1 + , 2 x, 1 ÷)
window size: ≤ 14 instructions ≤ 5 instructions
No issue on structural hazard same
WAR: renaming avoids stall completion
WAW: renaming avoids stall completion
Broadcast results from FU Write/read registers
Control: reservation stations central scoreboard

## Slide 34: Tomasulo Drawbacks
Complexity
Many associative writebacks (CDB) at high speed
  Big load for a single bus
  Can only writeback one result per clock
Performance limited by Common Data Bus
  Multiple CDBs => more FU logic for parallel assoc writebacks

## Slide 35: Tomasulo Loop Example
Loop: L.D F0 0 R1
MUL.D F4 F0 F2
S.D F4 0 R1
DADDI R1 R1 -8
BNEZ R1 Loop
Assumed latencies:
  Multiply - 4
  First load - 8 (e.g., cache miss)
  Subsequent loads - 4 (cache hit)
  Stores - 3
To be clear, will show clocks for DADDI, BNEZ
Assume branch predicted “taken”
Assume DADDI issue, execution, forwarding and write-back is done in one cycle (done to simplify this example).
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3
Notes: Note that times are from execute-to-ExecuteComplete

## Slide 36: Loop Example Cycle 0
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3
Notes: 2 iterations are “unrolled”
Assume
Predict taken
Int ALU ignored (except for issue time)

## Slide 37: Loop Example Cycle 1
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 38: Loop Example Cycle 2
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 39: Loop Example Cycle 3
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 40: Loop Example Cycle 4
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 41: Loop Example Cycle 5
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 42: Loop Example Cycle 6
Note: F0 never sees Load1 result
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 43: Loop Example Cycle 7
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 44: Loop Example Cycle 8
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 45: Loop Example Cycle 9
Load1 completing; what is waiting for it?
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 46: Loop Example Cycle 10
Load2 completing; what is waiting for it?
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 47: Loop Example Cycle 11
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3
Notes: Iteration 3 stalls on MUL.D as no reservation station is available.

## Slide 48: Loop Example Cycle 12
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3
Notes: Iteration 3 stalls on MUL.D as no reservation station is available.

## Slide 49: Loop Example Cycle 13
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3
Notes: Iteration 3 stalls on MUL.D as no reservation station is available.

## Slide 50: Loop Example Cycle 14
Mult2 completing; what is waiting for it?
Notes: Iteration 3 stalls on MUL.D as no reservation station is available.

## Slide 51: Loop Example Cycle 15
Mult2 completing; what is waiting for it?

## Slide 52: Loop Example Cycle 16
Much going on here. Can you tell what happened?

## Slide 53: Loop Example Cycle 17
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 54: Loop Example Cycle 18
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 55: Loop Example Cycle 19
Assumed ‘EX’ CC’s: First Load – 8, Subsequent – 4, Mult – 4, Stores – 3

## Slide 56: Tomasulo Summary
Reservations stations: renaming to larger set of registers + buffering source operands
  Prevents registers as bottleneck
  Avoids WAR, WAW hazards of Scoreboard
  Allows loop unrolling in HW
Not limited to basic blocks (integer units gets ahead, beyond branches)
Lasting Contributions
  Dynamic scheduling
  Register renaming
  Load/store disambiguation
360/91 descendants are Pentium II; PowerPC 604; MIPS R10000; HP-PA 8000; Alpha 21264

## Slide 57: ILP Summary (up to now)
Leverage Implicit Parallelism for Performance: Instruction Level Parallelism
Loop unrolling by compiler to increase ILP
Branch prediction to increase ILP
Dynamic HW exploiting ILP
  Works when can’t know dependence at compile time
  Can hide L1 cache misses
  Code for one machine runs well on another