## Slide 1
Research Update
2d Lt David Crow
Dr. Scott Graham

## Slide 2: Overview
Study 1 (complete*)
  Background
  Experiments
  Results
  Conclusions
Study 2 (ongoing)
  Background
  Demonstrated capabilities
  Thoughts going forward
*essentially

## Slide 3: Study 1
Can deep learning tools effectively determine which
vehicle generated a given segment of data?

## Slide 4: Controller Area Network

## Slide 5: Methodology
For each of three disparate experiments:
Process the data
Iteratively evaluate deep learning models (MLP, CNN)
Re-evaluate the optimal models
  Train/test using the full dataset
  Train/test using a balanced dataset

## Slide 6: Exp. 1: Ordered Data
 | … | 
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
Data | Data | Data | Data | … | … | … | … | … | …
Time
Input sample
1024 bytes

## Slide 7: Exp. 2: Ordered ArbIDs
 | … | 
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
ArbID | ArbID | ArbID | ArbID | … | … | … | … | … | …
Time
Input sample
N = 128

## Slide 8: Exp. 3: Unordered Data
 | … | 
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
Data | Data | Data | Data | … | … | … | … | … | …
Time
Input sample
1024 bytes

## Slide 9: Results
Model | Dataset | Ordered Data Accuracy3 | Ordered ArbIDs Accuracy | Unordered Data Accuracy
MLP1 | Imbalanced (full) | 94.46 % | 82.08 % | 59.26 %
MLP | Balanced | 67.48 % | 68.16 % | 42.04 %
CNN2 | Imbalanced (full) | 99.64 % | 99.52 % | 98.83 %
CNN | Balanced | 95.63 % | 99.05 % | 75.22 %
 | Average | 89.30 % | 87.20 % | 68.84 %
1Multilayer perceptron
2Convolutional neural network
3Balanced accuracy

## Slide 10: Conclusions
Deep learning models can effectively fingerprint vehicles
Deeper analysis of CAN design choices and tendencies
Intruder can employ deep learning for personal gain
Model | Dataset | Ordered Data Accuracy | Ordered ArbIDs Accuracy | Unordered Data Accuracy
CNN | Imbalanced | 99.64 % | 99.52 % | 98.83 %
Notes: Touch on limitations of the experiments/conclusions (e.g., small number of classes)

## Slide 11: Study 1 ⟶ Study 2
Study 1 assumes we only have access to raw CAN data
Study 2 assumes we can extract time series from the data

## Slide 12: Study 2
Can various empirical dynamic modeling (EDM) techniques
enable better analysis of a vehicle’s time series data?

## Slide 13: Time Series
(a) Google stock price for 200 consecutive days; (b) Daily change in the Google stock price for 200 consecutive days; (c) Annual number of strikes in the US; (d) Monthly sales of new one-family houses sold in the US; (e) Annual price of a dozen eggs in the US (constant dollars); (f) Monthly total of pigs slaughtered in Victoria, Australia; (g) Annual total of lynx trapped in the McKenzie River district of north-west Canada; (h) Monthly Australian beer production; (i) Monthly Australian electricity production.

## Slide 14: Empirical Dynamic Modeling

## Slide 15: Empirical Dynamic Modeling
Analyze the state space
Predict time series
Identify deterministic chaos
Characterize nonlinearity
Detect causality
1
3
4
5
2

## Slide 16: Reverse Engineering Pipeline
Notes: Mention that EDM should apply to any CPS (e.g., planes)

## Slide 17: Demonstrated Capabilities

## Slide 18: Demonstrated Capabilities

## Slide 19: Demonstrated Capabilities

## Slide 20: Demonstrated Capabilities

## Slide 21: Going Forward
Collect more simulated flight data
Ensure better understanding of implications of EDM
Identify states present in a system (e.g., takeoff, stall)?
Apply EDM methodology to further analyze CAN data*
Reach: establish preliminary intrusion detection system
*time series labels required for causality detection
Notes: Third bullet: this should help in reverse engineering

## Slide 22: Questions/Concerns