## Slide 1: Air Force Institute of Technology
Cyber-Physical System Intrusion: A Case Study of
Automobile Identification Vulnerabilities and
Automated Approaches for Intrusion Detection
2d Lt David Crow
GCS, ENG 20M, AFIT
Cyber-Physical System Intrusion: A Case Study of
Automobile Identification Vulnerabilities and
Automated Approaches for Intrusion Detection
2d Lt David Crow
GCS, ENG 20M, AFIT

## Slide 2: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 3: Motivation
An attacker familiar with the design of a specific vehicle’s
controller area network (CAN) can better attack the vehicle

## Slide 4: Research Question 1
Do the packets that broadcast on a vehicle’s
CAN bus uniquely identify the vehicle?

## Slide 5: Motivation
Intrusion detection systems (IDSs) are a common
method to protect computer networks from intrusion

## Slide 6: Research Question 2
Can we develop an effective IDS for a
cyber-physical system (CPS) like the CAN?

## Slide 7: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 8: Cyber-Physical Systems
“systems where the cyber parts, i.e., the computing and communication parts, and the physical parts are tightly integrated, both at the design time and during operation”
Difficult to replicate a CPS’s model ⟶ CPS monitoring
Output of CPS monitoring: time series data

## Slide 9: Time Series Data
“(a) Google stock price for 200 consecutive days; (b) Annual number of [labor] strikes in the US; (c) Annual price of a dozen eggs in the US (constant dollars); (d) Monthly total of pigs slaughtered in Victoria, Australia; (e) Annual total of lynx trapped in the McKenzie River district of north-west Canada; (f) Monthly Australian electricity production.”

## Slide 10: Deep Learning
Multilayer perceptrons (MLPs) and convolutional neural networks (CNNs) approximate a function
Both can classify (predict the class/category of) input
CNNs are specialized networks for processing data with a “grid-like topology”
CNNs are (generally) more complex and more powerful

## Slide 11: Neural Networks
A multilayer perceptron (MLP) approximates a function
Attempts to match predicted output to expected output for some given input
Uses general matrix multiplication to update weights on neurons
“An example of a feedforward network, drawn in two different styles ... It has a single hidden layer containing two units.”

## Slide 12: Convolutional Neural Network
A convolutional neural network (CNN) processes data with a “known grid-like topology”
Time series are 1-D grids
Uses convolution operation to update weights on neurons
“An example of 2-D convolution ..."

## Slide 13: Classification
For some input, predict one of classes
Often measure performance with accuracy

## Slide 14: Controller Area Network

## Slide 15: Intrusion Detection Systems
Monitors a network and alerts administrator of intrusion
Two primary types of IDSs
  Misuse detection
  Anomaly detection
Monitors a network and alerts administrator of intrusion
Two primary types of IDSs
  Misuse detection
  Anomaly detection

## Slide 16: Causality
Relationship between cause and effect
Difficult to measure/quantify
Approximate causality using statistical techniques
Notes: Causality matters because it’s a physical system

## Slide 17: Granger Causality
For two variables and :
does not precede in time
contains info that improves the prediction of
This info is not contained in any other series
Difficult to confirm these ⟶ predict with

## Slide 18: Empirical Dynamic Modeling
Panel A
Lorenz system manifold
Projection of dimension
Panel B
and two -lags of
Shadow manifold
and are diffeomorphic

## Slide 19: Empirical Dynamic Modeling
Convergent cross-mapping (CCM)
Original manifold
Shadow manifolds ,
, , are diffeomorphic

## Slide 20: Related Work
CAN security
Predict future CAN data
Classify CAN data samples as normal/abnormal
Classify drivers using reverse-engineered CAN data
Granger causality
Correlate/aggregate alerts to identify important alerts
Determine variables which best predict an attack
Empirical dynamic modeling
None!

## Slide 21: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 22: Experimental Data
11 vehicles
230 MB of CAN data
Arbitration identifier (arbID)
Hexadecimal data
Vehicle | Make | Model | Year
1 | Chevrolet | Cobalt | 2009
2 | Chevrolet | Silverado | 2011
3 | Dodge | 1500 | 2014
4 | Ford | F-150 | 2017
5 | Ford | Focus | 2010
6 | Honda | Accord | 2012
7 | Honda | Accord | 2015
8 | Nissan | 370Z | 2015
9 | Nissan | XTERRA | 2010
10 | Saab | 9-7X | 2009
11 | Toyota | Corolla | 2009

## Slide 23: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 24: Methodology
For each of three disparate experiments:
Process the data
Iteratively train and evaluate deep learning models
Re-evaluate the optimal models
  Train/test using the full dataset
  Train/test using a balanced dataset

## Slide 25: Exp. 1: Ordered Data
 | … | 
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
Data | Data | Data | Data | … | … | … | … | … | …
Time
Input sample
1024 bytes

## Slide 26: Exp. 2: Ordered ArbIDs
 | … | 
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
ArbID | ArbID | ArbID | ArbID | … | … | … | … | … | …
Time
Input sample
N = 128

## Slide 27: Exp. 3: Unordered Data
 | … | 
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
CAN packet |  | 
ArbID | … | Data
Data | Data | Data | Data | … | … | … | … | … | …
Time
Input sample
1024 bytes

## Slide 28: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 29: Results
Model | Dataset | Ordered Data Balanced Accuracy | Ordered ArbIDs Balanced Accuracy | Unordered Data Balanced Accuracy
MLP | Imbalanced (full) | 94.46 % | 82.08 % | 59.26 %
MLP | Balanced | 67.48 % | 68.16 % | 42.04 %
CNN | Imbalanced (full) | 99.64 % | 99.52 % | 98.83 %
CNN | Balanced | 95.63 % | 99.05 % | 75.22 %
 | Average | 89.30 % | 87.20 % | 68.84 %

## Slide 30: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 31: Intrusion Detection Systems
IDS architects require the following:
Insight into the dynamics of a CPS, to include an understanding of the way in which some current state enables predictions concerning a future state
An ample quantity of data obtained under normal operating conditions to establish normal behavior
A process to determine whether new traffic conforms to normal behavior
An alert system to report to the administrator the traffic that does not conform
IDS architects require the following:
Insight into the dynamics of a CPS, to include an understanding of the way in which some current state enables predictions concerning a future state
An ample quantity of data obtained under normal operating conditions to establish normal behavior
A process to determine whether new traffic conforms to normal behavior
An alert system to report to the administrator the traffic that does not conform

## Slide 32: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 33: Linear Data – Steering System
Notes: Be very explicit about mathematical model vs. simulation (and why this model is limited)

## Slide 34: Nonlinear Data – Flight Simulator

## Slide 35: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 36: Granger Causality
Utilize StatsModels’ grangercausalitytests
Null hypothesis: “ does not Granger-cause ”
Reject null hypothesis if (on average)
Vary the parameter maxlag

## Slide 37: Empirical Dynamic Modeling
Suggested methodology:
Conduct nearest neighbor forecasting via simplex projection to identify the embedding dimension which maximizes the prediction skill
Use simplex projection and to determine whether the system exhibits deterministic chaos
Employ sequential locally weighted global linear maps (S-maps) to characterize any nonlinearity in the data
Utilize CCM to evaluate predictive accuracy and quantify (estimate) causality

## Slide 38: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 39: Linear Data – Granger
Granger causality between each pair of steering system time series.

## Slide 40: Linear Data – EDM
Plots illustrating the optimal embedding dimension for each steering system time series.

## Slide 41: Linear Data – EDM
Plots illustrating the deterministic chaos present in each steering system time series.

## Slide 42: Linear Data – EDM
Plots illustrating the nonlinearity of each steering system time series.

## Slide 43: Linear Data – EDM
Plots illustrating the predictions
for each steering system time series.
Plots illustrating the prediction error
for each steering system time series.
Notes: Be specific about “next-point predictions”

## Slide 44: Linear Data – EDM
Time Series | Naive Error | EDM Error
Steering wheel angle | 0.009424 | 0.003351
Left wheel RPM | 0.005742 | 0.003893
Right wheel RPM | 0.005742 | 0.003893
Plots illustrating the predictions
for each steering system time series.
Naive and EDM root-mean-square error
for each steering system time series.

## Slide 45: Linear Data – EDM
Plots illustrating the causality between each pair of steering system time series.

## Slide 46: Linear Data – EDM
Plots illustrating predictive capability by analyzing the causality
between each pair of steering system time series.

## Slide 47: Nonlinear Data – Granger
Granger causality between each pair of selected AVAS time series.

## Slide 48: Nonlinear Data – EDM
Plots illustrating the optimal embedding dimension for each selected AVAS time series.

## Slide 49: Nonlinear Data – EDM
Plots illustrating the deterministic chaos present in each selected AVAS time series.

## Slide 50: Nonlinear Data – EDM
Plots illustrating the nonlinearity of each selected AVAS time series.

## Slide 51: Nonlinear Data – EDM
Plots illustrating the predictions
for each selected AVAS time series.
Plots illustrating the prediction error
for each selected AVAS time series.

## Slide 52: Nonlinear Data – EDM
Time Series | Naive Error | EDM Error
Airspeed | 3.907005 | 0.070161
Altitude | 18.192201 | 0.001535
Pitch | 0.013749 | 0.019748
Plots illustrating the predictions
for each selected AVAS time series.
Naive and EDM root-mean-square error
for each selected AVAS time series.

## Slide 53: Nonlinear Data – EDM
Plots illustrating the causality between each pair of selected AVAS time series.

## Slide 54: Nonlinear Data – EDM
Plots illustrating predictive capability by analyzing the causality
between each pair of selected AVAS time series.

## Slide 55: Overview
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 56: Conclusions
Question 1: Do CAN packets uniquely identify a vehicle?
Yes; deep learning tools can classify raw CAN data
This risks privacy and safety
Question 2: Can we develop an IDS for a CPS like the CAN?
Maybe; insight into the CPS’s behavior could enable an IDS
Granger causality does not seem to enable this insight
Linear systems are probably too simplistic for EDM
EDM may suffice for nonlinear systems
Notes: Discuss MLPs vs. CNNs

## Slide 57: Future Work
Identifying vehicles
Apply this methodology to a much larger dataset
Train a Siamese neural network to classify CAN samples
Detecting intrusion
Address the remaining steps towards an IDS
Evaluate more robust datasets/CPSs
Explore other time series analysis techniques

## Slide 58: Contributions
First demonstration of the unique signature of a vehicle’s raw CAN data and a discussion of the associated risks
First in-depth presentation of advantages/disadvantages of Granger causality and EDM for linear/nonlinear data
First argument for applying EDM to IDS development
First complete library of EDM functions for use with standardized time series data
Publications
(accepted) ICCWS 2020
(pending) IFIP Critical Infrastructure Protection 2020

## Slide 59: Summary
Motivation
Background & related work
Identifying vehicles
  Experimental data
  Methodology
  Results
Detecting intrusion
  Experimental data
  Methodology
  Results
Conclusions

## Slide 60: References
ACM Transactions on Cyber-Physical Systems, “Cyber-Physical Systems (TCPS): About,” 2018. [Online]. Available: https://tcps.acm.org/about.cfm [Accessed: 2019-05-31]
BiObserver, “Visualization of Granger causality,” 2014. [Online]. Available: https: //commons.wikimedia.org/wiki/File:GrangerCausalityIllustration.svg [Accessed: 2019-09-27]
G. E. P. Box, G. M. Jenkins, and G. C. Reinsel, Time Series Analysis: Forecasting and Control. Upper Saddle River, New Jersey, USA: Prentice-Hall, Inc., 1994.
A. Burkov, The Hundred-Page Machine Learning Book. Andriy Burkov, 2019.
J. B. Cabrera, L. Lewis, X. Qin, W. Lee, and R. K. Mehra, “Proactive Intrusion Detection and Distributed Denial of Service Attacks - A Case Study in Security Management,” Journal of Network and Systems Management, vol. 10, no. 2, pp. 225–254, 2002.
J. B. Cabrera, L. Lewis, X. Qin, W. Lee, R. K. Prasanth, B. Ravichandran, and R. K. Mehra, “Proactive detection of distributed denial of service attacks using MIB traffic variables-a feasibility study,” 2001 7th IEEE/IFIP International Symposium on Integrated Network Management Proceedings: Integrated Management Strategies for the New Millennium, vol. 00, no. c, pp. 609–622, 2001.
M. Enev, A. Takakuwa, K. Koscher, and T. Kohno, “Automobile Driver Finger- printing,” in Proceedings on Privacy Enhancing Technologies, vol. 2016, no. 1, 2015, pp. 34–50.
I. Goodfellow, Y. Bengio, and A. Courville, Deep Learning. Cambridge, Massachusetts, USA: The MIT Press, 2016.
C. W. J. Granger, “Investigating Causal Relations By Econometric Models,” Econometrica, vol. 37, no. 3, pp. 424–438, 1969.
R. J. Hyndman and G. Athanasopoulos, Forecasting: Principles and Practice, 2nd ed. Melbourne, Australia: OTexts, 2018.
M. J. Kang and J. W. Kang, “Intrusion Detection System Using Deep Neural Network for In-Vehicle Network Security,” PLoS ONE, vol. 11, no. 6, pp. 1–17, 2016.
D. Kwon, H. Kim, J. Kim, S. C. Suh, I. Kim, and K. J. Kim, “A survey of deep learning-based network anomaly detection,” Cluster Computing, pp. 1–13, 2017.
J. M. Lee, Introduction to Topological Manifolds, 2nd ed. New York, New York, USA: Springer US, 2011.

## Slide 61: References
M. Marchetti and D. Stabili, “Anomaly detection of CAN bus messages through analysis of ID sequences,” in 2017 IEEE Intelligent Vehicles Symposium (IV). IEEE, 2017, pp. 1577–1583.
National Instruments, “Controller Area Network (CAN) Overview,” 2019. [Online]. Available: https://www.ni.com/en-us/innovations/white-papers/06/controller-area-network--can--overview.html [Accessed: 2019-07-08]
C. Nicholson, “A Beginner’s Guide to Neural Networks and Deep Learning,” 2019. [Online]. Available: https://skymind.ai/wiki/neural-network [Accessed: 2019-09-26]
J. Perktold, S. Seabold, and J. Taylor, “StatsModels: Statistics in Python,” 2009.
X. Qin and W. Lee, “Statistical Causality Analysis of Infosec Alert Data,” in International Workshop on Recent Advances in Intrusion Detection. Springer Berlin Heidelberg, 2003, pp. 73–93.
B. Stone, S. Graham, B. Mullins, and C. Schubert Kabban, “Enabling Auditing and Intrusion Detection for Proprietary Controller Area Networks,” Dissertation, Air Force Institute of Technology, 2018.
Sugihara Lab: Quantitative Ecology and Data-Driven Theory, “Empirical Dynamic Modeling,” 2019. [Online]. Available: http://deepecoweb.ucsd.edu/ nonlinear-dynamics-research/edm/ [Accessed: 2019-05-31]
G. Sugihara, “Nonlinear forecasting for the classification of natural time series,” Philosophical Transactions of the Royal Society: Mathematical, Physical and Engineering Sciences, vol. 348, no. 1688, 1994.
G. Sugihara and R. May, “Nonlinear forecasting as a way of distinguishing chaos from measurement error in time series,” Nature, vol. 344, pp. 734–741, 1990.
G. Sugihara, R. May, H. Ye, C.-h. Hsieh, E. Deyle, M. Fogarty, and S. Munch, “Detecting Causality in Complex Ecosystems,” Science, vol. 338, no. October, pp. 496–500, 2012.
Z. Tyree, R. A. Bridges, F. L. Combs, and M. R. Moore, “Exploiting the Shape of CAN Data for In-Vehicle Intrusion Detection,” in 2018 IEEE 88th Vehicular Technology Conference (VTC-Fall), 2019, pp. 1–5.
H. Ye, A. Clarke, E. Deyle, and G. Sugihara, “rEDM: An R package for Empirical Dynamic Modeling and Convergent Cross Mapping,” pp. 1–19, 2019. [Online]. Available: https://cran.r-project.org/web/packages/rEDM/vignettes/rEDM.html [Accessed: 2019-12-12]

## Slide 62: Air Force Institute of Technology
Cyber-Physical System Intrusion: A Case Study of
Automobile Identification Vulnerabilities and
Automated Approaches for Intrusion Detection
2d Lt David Crow